====================================================================================================
====================================================================================================
===AT TIME= 236.25 FLAPS LAND =======================================================================
====================================================================================================
====================================================================================================
flight control ptch: 0.1716 ratio
flight control hdng: 0.0028 ratio
flight control roll: 0.0170 ratio

h : 322 m
rho : 1.1876 kg/cubic meter, density ratio: 0.9694
vx : 27.9
vy : -1.0
vz : -10.0
mach-1 : 339.0 m/s
airspeed: 29.6 m/s
mach : 0.0874

psi : 70.1 deg
the : -2.2 deg
phi : 1.6 deg

alpha : -0.2 deg (pos nose up)
beta : -0.2 deg (pos nose right)

P : 0.6 deg/second
Q : 0.0 deg/second
R : 0.4 deg/second

tire height above ground : 322 m
resting height of aircraft above ground: 0 m

LEFT WING 1 height above ground: 323.56 m
hgt_in_cords is 421.2524
hgt_in_spans is 18.3110
setting ground effect cl multiplier to 1.0002
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 1 height above ground: 323.41 m
hgt_in_cords is 421.0569
hgt_in_spans is 18.3025
setting ground effect cl multiplier to 1.0002
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT WING 2 height above ground: 323.92 m
hgt_in_cords is 568.2971
hgt_in_spans is 18.3310
setting ground effect cl multiplier to 1.0002
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 2 height above ground: 323.52 m
hgt_in_cords is 567.6080
hgt_in_spans is 18.3088
setting ground effect cl multiplier to 1.0002
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT H STAB height above ground: 324.02 m
hgt_in_cords is 708.7015
hgt_in_spans is 96.3176
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT H STAB height above ground: 323.99 m
hgt_in_cords is 708.6309
hgt_in_spans is 96.3080
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

----------------------------------------------------------------------------------------------------
---RUNNING PROPULSIVE FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM---------------------------
----------------------------------------------------------------------------------------------------
Before all propulsion:
f_axil= 0.0 N, pos aft, L= 0.0 N-m, pos right
f_side= 0.0 N, pos right, M= 0.0 N-m, pos up
f_nrml= 0.0 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.7 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.1 vz= 29.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.3
incidence : 4.0
incidence increase : 0.0
geometric alpha : 3.7
v for forces : 29.7 (based on effective sweep of -1.0 deg)

   FLAPS #1: crat= 0.1400, def= 50.0 deg: (pos down or extended, neg up)
dx_te = 0.9500
dy_te = 0.1072
al_inc= 5.4323
cl inc= 0.3966
cd inc= 0.0030
cm inc=-0.3966
Effective alpha increased 5.4 deg by all combined lift-incrementation devices up to final geo alpha of 9.1 deg

AR=31.0561, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number:	Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using tables 0 and 1
That's the tables for Re= 1.1000 million and Re= 1.4000 million, with flight Re= 1.3301 million
alpha airflow= 9.1, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 8.8
alpha airflow= 9.1, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 8.8
Cl lookups: 1.2246 and 1.0660, interpolated Cl= 1.1030
Cd lookups: 0.0078 and 0.0085, interpolated Cd= 0.0083
Cm lookups: -0.0406 and -0.0406, interpolated Cm=-0.0406

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.3301 1.3301 |
        reyno 2 1.3301 1.3301 |======>with flight Re= 1.3301 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.1030 1.1030 |
        reyno 2 1.1030 1.1030 |======>resultant cl= 1.1030

CD coeff summary: ---------- -root --tip
        reyno 1 0.0083 0.0083 |
        reyno 2 0.0083 0.0083 |======>resultant cd= 0.0083

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0406 -0.0406 |
        reyno 2 -0.0406 -0.0406 |======>resultant cm=-0.0406

adding control-effects cl of 0.3966 takes cl to 1.4996
adding control-effects cd of 0.0030 takes cd to 0.0113
adding control-effects cm of -0.3966 takes cm to -0.4373
finite-wing lift multiplier of 0.9801 takes cl to 1.4697, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0561, gives cdi of 0.0238

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.4757* 3.5864* sqr( 29.7) * 1.1876 / 2 = 2763.9 N
drag= 0.0351* 3.5864* sqr( 29.7) * 1.1876 / 2 = 65.8 N
momt=-0.4389* 3.5864* sqr( 29.7) * 1.1876 / 2 * 0.67= -554.0 N-m

LEFT WING 1:

x= -2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2763.9 N pos up.
drag_local_path= 65.8 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0524 0.9986 0.0050
drag vector xyz=-0.0040 -0.0048 1.0000
side vector xyz= 0.9986 -0.0524 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 1
f_axil= 79.6 N, pos aft, L= 7486.1 N-m, pos right
f_side= 144.6 N, pos right, M= -510.0 N-m, pos up
f_nrml= 2759.8 N, pos up, N= -242.6 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.2
incidence : 4.0
incidence increase : 0.0
geometric alpha : 3.8
v for forces : 29.6 (based on effective sweep of 1.0 deg)

   FLAPS #1: crat= 0.1400, def= 50.0 deg: (pos down or extended, neg up)
dx_te = 0.9500
dy_te = 0.1072
al_inc= 5.4323
cl inc= 0.3964
cd inc= 0.0030
cm inc=-0.3964
Effective alpha increased 5.4 deg by all combined lift-incrementation devices up to final geo alpha of 9.3 deg

AR=31.0561, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number:	Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using tables 0 and 1
That's the tables for Re= 1.1000 million and Re= 1.4000 million, with flight Re= 1.3287 million
alpha airflow= 9.3, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 8.9
alpha airflow= 9.3, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 8.9
Cl lookups: 1.2408 and 1.0779, interpolated Cl= 1.1166
Cd lookups: 0.0078 and 0.0085, interpolated Cd= 0.0083
Cm lookups: -0.0406 and -0.0406, interpolated Cm=-0.0406

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.3287 1.3287 |
        reyno 2 1.3287 1.3287 |======>with flight Re= 1.3287 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.1166 1.1166 |
        reyno 2 1.1166 1.1166 |======>resultant cl= 1.1166

CD coeff summary: ---------- -root --tip
        reyno 1 0.0083 0.0083 |
        reyno 2 0.0083 0.0083 |======>resultant cd= 0.0083

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0406 -0.0406 |
        reyno 2 -0.0406 -0.0406 |======>resultant cm=-0.0406

adding control-effects cl of 0.3964 takes cl to 1.5130
adding control-effects cd of 0.0030 takes cd to 0.0113
adding control-effects cm of -0.3964 takes cm to -0.4370
finite-wing lift multiplier of 0.9801 takes cl to 1.4828, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0561, gives cdi of 0.0243

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.4889* 3.5864* sqr( 29.6) * 1.1876 / 2 = 2782.7 N
drag= 0.0356* 3.5864* sqr( 29.6) * 1.1876 / 2 = 66.5 N
momt=-0.4386* 3.5864* sqr( 29.6) * 1.1876 / 2 * 0.67= -552.5 N-m

RIGT WING 1:

x= 2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2782.7 N pos up.
drag_local_path= 66.5 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0524 0.9986 0.0027
drag vector xyz=-0.0040 -0.0029 1.0000
side vector xyz= 0.9986 0.0524 0.0041

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 1
f_axil= 153.5 N, pos aft, L= -51.6 N-m, pos right
f_side= -1.4 N, pos right, M= -1022.5 N-m, pos up
f_nrml= 5538.4 N, pos up, N= -15.3 N-m, pos right
----------------------------------------------------------------------------------------------------

•••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.2 vz of 29.7 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.2 vz= 29.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.4
incidence : 4.0
incidence increase : 0.0
geometric alpha : 3.6
v for forces : 29.6 (based on effective sweep of -3.4 deg)

   AILERON #1: crat= 0.1500, def= 0.5 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te = 0.0013
al_inc= 0.0613
cl inc= 0.0170
cd inc= 0.0000
cm inc=-0.0115
Effective alpha increased 0.1 deg by all combined lift-incrementation devices up to final geo alpha of 3.7 deg

AR=31.0561, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.8431 million
alpha airflow= 3.7, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 3.5
Cl lookup: 0.4985
Cd lookup: 0.0078
Cm lookup: -0.0432

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.8431 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.4985 0.4985 |
        reyno 2 0.4985 0.4985 |======>resultant cl= 0.4985

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0432 -0.0432 |
        reyno 2 -0.0432 -0.0432 |======>resultant cm=-0.0432

adding control-effects cl of 0.0170 takes cl to 0.5155
adding control-effects cd of 0.0000 takes cd to 0.0079
adding control-effects cm of -0.0115 takes cm to -0.0547
finite-wing lift multiplier of 0.9801 takes cl to 0.5052, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0561, gives cdi of 0.0028

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.5073* 1.3372* sqr( 29.6) * 1.1876 / 2 = 353.7 N
drag= 0.0107* 1.3372* sqr( 29.6) * 1.1876 / 2 = 7.4 N
momt=-0.0549* 1.3372* sqr( 29.6) * 1.1876 / 2 * 0.43= -16.4 N-m

LEFT WING 2:

x= -7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 353.7 N pos up.
drag_local_path= 7.4 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0527 0.9986 0.0065
drag vector xyz=-0.0040 -0.0063 1.0000
side vector xyz= 0.9986 -0.0527 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 2
f_axil= 163.3 N, pos aft, L= 2437.4 N-m, pos right
f_side= 17.2 N, pos right, M= -1082.7 N-m, pos up
f_nrml= 5891.6 N, pos up, N= -87.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.0 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.0 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.1
incidence : 4.0
incidence increase : 0.0
geometric alpha : 3.9
v for forces : 29.6 (based on effective sweep of 3.4 deg)

   AILERON #1: crat= 0.1500, def= -0.5 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te =-0.0013
al_inc=-0.0613
cl inc=-0.0170
cd inc= 0.0000
cm inc= 0.0115
Effective alpha increased -0.1 deg by all combined lift-incrementation devices up to final geo alpha of 3.9 deg

AR=31.0561, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.8408 million
alpha airflow= 3.9, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 3.7
Cl lookup: 0.5221
Cd lookup: 0.0078
Cm lookup: -0.0431

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.8408 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.5221 0.5221 |
        reyno 2 0.5221 0.5221 |======>resultant cl= 0.5221

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0431 -0.0431 |
        reyno 2 -0.0431 -0.0431 |======>resultant cm=-0.0431

adding control-effects cl of -0.0170 takes cl to 0.5051
adding control-effects cd of 0.0000 takes cd to 0.0078
adding control-effects cm of 0.0115 takes cm to -0.0317
finite-wing lift multiplier of 0.9801 takes cl to 0.4950, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0561, gives cdi of 0.0027

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.4970* 1.3372* sqr( 29.6) * 1.1876 / 2 = 344.7 N
drag= 0.0105* 1.3372* sqr( 29.6) * 1.1876 / 2 = 7.3 N
momt=-0.0318* 1.3372* sqr( 29.6) * 1.1876 / 2 * 0.43= -9.4 N-m

RIGT WING 2:

x= 7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 344.7 N pos up.
drag_local_path= 7.3 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0524 0.9986 0.0011
drag vector xyz=-0.0040 -0.0013 1.0000
side vector xyz= 0.9986 0.0524 0.0041

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 2
f_axil= 171.0 N, pos aft, L= 11.4 N-m, pos right
f_side= -0.9 N, pos right, M= -1136.6 N-m, pos up
f_nrml= 6235.8 N, pos up, N= -30.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.2 vz of 29.7 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.2 vz= 29.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.3
incidence : 0.0
incidence increase : 0.0
geometric alpha : -0.3
v for forces : 27.6 (based on effective sweep of -22.0 deg)

AR=31.0108, e= 0.9363, ls_D_ls0= 0.9409, al_D_al0= 0.9601, cl_D_cl0= 0.9800

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3645 million
alpha airflow= -0.3, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= -0.3
Cl lookup: -0.0333
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3645 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.0333 -0.0333 |
        reyno 2 -0.0333 -0.0333 |======>resultant cl=-0.0333

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9800 takes cl to -0.0326, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0108, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.0328* 0.0502* sqr( 27.6) * 1.1876 / 2 = -0.7 N
drag= 0.0010* 0.0502* sqr( 27.6) * 1.1876 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 27.6) * 1.1876 / 2 * 0.20= 0.0 N-m

LEFT WING 3:

x= -8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= -0.7 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9708 0.2397 0.0056
drag vector xyz=-0.0041 -0.0069 1.0000
side vector xyz= 0.2397 -0.9708 -0.0057

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= 171.0 N, pos aft, L= 9.1 N-m, pos right
f_side= -1.6 N, pos right, M= -1136.5 N-m, pos up
f_nrml= 6235.6 N, pos up, N= -30.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.2 vz of 29.7 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.2 vz= 29.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.4
incidence : 0.0
incidence increase : 0.0
geometric alpha : -0.4
v for forces : 27.6 (based on effective sweep of -22.0 deg)

AR=31.0108, e= 0.9363, ls_D_ls0= 0.9409, al_D_al0= 0.9601, cl_D_cl0= 0.9800

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2728 million
alpha airflow= -0.4, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= -0.3
Cl lookup: -0.0337
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2728 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.0337 -0.0337 |
        reyno 2 -0.0337 -0.0337 |======>resultant cl=-0.0337

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9800 takes cl to -0.0330, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0108, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.0331* 0.0374* sqr( 27.6) * 1.1876 / 2 = -0.6 N
drag= 0.0010* 0.0374* sqr( 27.6) * 1.1876 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 27.6) * 1.1876 / 2 * 0.15= 0.0 N-m

LEFT WING 3:

x= -8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= -0.6 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9708 0.2397 0.0057
drag vector xyz=-0.0041 -0.0069 1.0000
side vector xyz= 0.2397 -0.9708 -0.0057

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= 171.0 N, pos aft, L= 7.1 N-m, pos right
f_side= -2.1 N, pos right, M= -1136.5 N-m, pos up
f_nrml= 6235.4 N, pos up, N= -29.9 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.0 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.0 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.2
incidence : 0.0
incidence increase : 0.0
geometric alpha : 0.2
v for forces : 27.5 (based on effective sweep of 22.0 deg)

AR=30.9875, e= 0.9363, ls_D_ls0= 0.9409, al_D_al0= 0.9600, cl_D_cl0= 0.9800

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3625 million
alpha airflow= 0.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9600, slat alpha divisor= 1.0000, alpha lookup= 0.2
Cl lookup: 0.0225
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3625 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0225 0.0225 |
        reyno 2 0.0225 0.0225 |======>resultant cl= 0.0225

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9800 takes cl to 0.0220, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 30.9875, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0221* 0.0502* sqr( 27.5) * 1.1876 / 2 = 0.5 N
drag= 0.0010* 0.0502* sqr( 27.5) * 1.1876 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 27.5) * 1.1876 / 2 * 0.20= 0.0 N-m

RIGT WING 3:

x= 8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= 0.5 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9699 0.2434 -0.0038
drag vector xyz=-0.0041 -0.0007 1.0000
side vector xyz= 0.2434 0.9699 0.0017

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= 171.0 N, pos aft, L= 5.6 N-m, pos right
f_side= -2.6 N, pos right, M= -1136.5 N-m, pos up
f_nrml= 6235.6 N, pos up, N= -29.6 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.0 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.0 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.2
incidence : 0.0
incidence increase : 0.0
geometric alpha : 0.2
v for forces : 27.5 (based on effective sweep of 22.0 deg)

AR=30.9875, e= 0.9363, ls_D_ls0= 0.9409, al_D_al0= 0.9600, cl_D_cl0= 0.9800

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2713 million
alpha airflow= 0.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9600, slat alpha divisor= 1.0000, alpha lookup= 0.2
Cl lookup: 0.0229
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2713 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0229 0.0229 |
        reyno 2 0.0229 0.0229 |======>resultant cl= 0.0229

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9800 takes cl to 0.0225, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 30.9875, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0225* 0.0374* sqr( 27.5) * 1.1876 / 2 = 0.4 N
drag= 0.0010* 0.0374* sqr( 27.5) * 1.1876 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 27.5) * 1.1876 / 2 * 0.15= 0.0 N-m

RIGT WING 3:

x= 8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= 0.4 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9699 0.2434 -0.0039
drag vector xyz=-0.0042 -0.0007 1.0000
side vector xyz= 0.2434 0.9699 0.0017

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= 171.0 N, pos aft, L= 4.3 N-m, pos right
f_side= -3.0 N, pos right, M= -1136.5 N-m, pos up
f_nrml= 6235.7 N, pos up, N= -29.3 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 3.8 deg, at v= 29.6 m/s for vertical delta= -1.97 m/s
So speed is changed to vx= -0.1 vy= -2.1 vz= 29.6 m/s
So final speed is vx= -0.1 vy= -2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : -4.0
incidence : -3.0
incidence increase : 0.0
geometric alpha : -7.0
v for forces : 29.6 (based on effective sweep of -4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -4.8 deg: (pos down or extended, neg up)
dx_te = 0.9986
dy_te =-0.0335
al_inc=-1.5375
cl inc=-0.2025
cd inc= 0.0001
cm inc= 0.1114
Effective alpha increased -1.5 deg by all combined lift-incrementation devices up to final geo alpha of -8.6 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.6971 million
alpha airflow= -8.6, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -6.7
Cl lookup: -0.7986
Cd lookup: 0.0081
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.6971 million
alpha airflow= -8.6, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -6.7
Cl lookup: -0.6988
Cd lookup: 0.0074
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.6971 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.7986 -0.6988 |
        reyno 2 -0.7986 -0.6988 |======>resultant cl=-0.7487

CD coeff summary: ---------- -root --tip
        reyno 1 0.0081 0.0074 |
        reyno 2 0.0081 0.0074 |======>resultant cd= 0.0077

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.2025 takes cl to -0.9512
adding control-effects cd of 0.0001 takes cd to 0.0079
adding control-effects cm of 0.1114 takes cm to 0.1114
finite-wing lift multiplier of 0.8884 takes cl to -0.8450, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0564

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.8481* 0.3906* sqr( 29.6) * 1.1876 / 2 = -172.9 N
drag= 0.0643* 0.3906* sqr( 29.6) * 1.1876 / 2 = 13.1 N
momt= 0.1136* 0.3906* sqr( 29.6) * 1.1876 / 2 * 0.35= 8.2 N-m

LEFT H STAB:

x= -0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -172.9 N pos up.
drag_local_path= 13.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0049 0.9975 0.0701
drag vector xyz=-0.0033 -0.0701 0.9975
side vector xyz= 1.0000 -0.0051 0.0029

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT H STAB
f_axil= 172.0 N, pos aft, L= -96.3 N-m, pos right
f_side= -3.9 N, pos right, M= -482.1 N-m, pos up
f_nrml= 6062.3 N, pos up, N= -26.6 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from RIGT WING 1 el #0 is 3.8 deg, at v= 29.6 m/s for vertical delta= -1.98 m/s
So speed is changed to vx= -0.1 vy= -2.1 vz= 29.6 m/s
So final speed is vx= -0.1 vy= -2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : -4.0
incidence : -3.0
incidence increase : 0.0
geometric alpha : -7.0
v for forces : 29.7 (based on effective sweep of 4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -4.8 deg: (pos down or extended, neg up)
dx_te = 0.9986
dy_te =-0.0335
al_inc=-1.5375
cl inc=-0.2025
cd inc= 0.0001
cm inc= 0.1113
Effective alpha increased -1.5 deg by all combined lift-incrementation devices up to final geo alpha of -8.6 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.6973 million
alpha airflow= -8.6, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -6.7
Cl lookup: -0.7994
Cd lookup: 0.0081
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.6973 million
alpha airflow= -8.6, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -6.7
Cl lookup: -0.6995
Cd lookup: 0.0074
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.6973 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.7994 -0.6995 |
        reyno 2 -0.7994 -0.6995 |======>resultant cl=-0.7494

CD coeff summary: ---------- -root --tip
        reyno 1 0.0081 0.0074 |
        reyno 2 0.0081 0.0074 |======>resultant cd= 0.0077

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.2025 takes cl to -0.9519
adding control-effects cd of 0.0001 takes cd to 0.0079
adding control-effects cm of 0.1113 takes cm to 0.1113
finite-wing lift multiplier of 0.8884 takes cl to -0.8456, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0565

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.8488* 0.3906* sqr( 29.7) * 1.1876 / 2 = -173.1 N
drag= 0.0644* 0.3906* sqr( 29.7) * 1.1876 / 2 = 13.1 N
momt= 0.1136* 0.3906* sqr( 29.7) * 1.1876 / 2 * 0.35= 8.2 N-m

RIGT H STAB:

x= 0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -173.1 N pos up.
drag_local_path= 13.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0049 0.9975 0.0703
drag vector xyz=-0.0033 -0.0703 0.9975
side vector xyz= 1.0000 0.0046 0.0036

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT H STAB
f_axil= 172.9 N, pos aft, L= 4.3 N-m, pos right
f_side= -3.1 N, pos right, M= 173.1 N-m, pos up
f_nrml= 5888.8 N, pos up, N= -29.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••VERT STAB 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.00 m, pos right from CG
element y= 0.45 m, pos up from CG
element z= 3.64 m, pos aft from CG

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 3.9 deg, at v= 29.6 m/s for vertical delta= -2.04 m/s
So speed is changed to vx= -0.1 vy= -2.2 vz= 29.6 m/s
WAKEWASH from LEFT WING 1 el #0 with cd= 0.0113, dy_chords= 0.08, wake_width_chords= 0.16, wake_deficit_at_center= 0.0520, wake_deficit_here= 0.0267, speed ratio= 0.9865
So speed is changed to vx= -0.1 vy= -2.1 vz= 29.2 m/s
So final speed is vx= -0.1 vy= -2.1 vz= 29.2 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.2
incidence : 0.0
incidence increase : 0.0
geometric alpha : 0.2
v for forces : 29.2 (based on effective sweep of 9.9 deg)

   RUDDER #1: crat= 0.3000, def= 0.1 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te = 0.0004
al_inc= 0.0166
cl inc= 0.0030
cd inc= 0.0000
cm inc=-0.0018
Effective alpha increased 0.0 deg by all combined lift-incrementation devices up to final geo alpha of 0.2 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_3m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 1.5645 million
alpha airflow= 0.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= 0.2
Cl lookup: 0.0150
Cd lookup: 0.0054
Cm lookup: 0.0000

root hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.5645 million
alpha airflow= 0.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= 0.2
Cl lookup: 0.0150
Cd lookup: 0.0046
Cm lookup: 0.0000

tip hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.5645 million
alpha airflow= 0.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= 0.2
Cl lookup: 0.0150
Cd lookup: 0.0046
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 3.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 1.5645 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0150 0.0150 |
        reyno 2 0.0150 0.0150 |======>resultant cl= 0.0150

CD coeff summary: ---------- -root --tip
        reyno 1 0.0054 0.0054 |
        reyno 2 0.0046 0.0046 |======>resultant cd= 0.0054

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of 0.0030 takes cl to 0.0180
adding control-effects cd of 0.0000 takes cd to 0.0054
adding control-effects cm of -0.0018 takes cm to -0.0018
finite-wing lift multiplier of 0.8884 takes cl to 0.0160, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0160* 0.9612* sqr( 29.2) * 1.1876 / 2 = 7.8 N
drag= 0.0054* 0.9612* sqr( 29.2) * 1.1876 / 2 = 2.6 N
momt=-0.0018* 0.9612* sqr( 29.2) * 1.1876 / 2 * 0.81= -0.7 N-m

VERT STAB 1:

x= -0.00 m pos right.
y= 0.45 m pos up.
z= 3.64 m pos aft.

lift_local_path= 7.8 N pos up.
drag_local_path= 2.6 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-1.0000 0.0005 -0.0031
drag vector xyz=-0.0031 -0.0725 0.9974
side vector xyz= 0.0003 0.9974 0.0725

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
VERT STAB 1
f_axil= 175.5 N, pos aft, L= 0.8 N-m, pos right
f_side= -10.9 N, pos right, M= 174.9 N-m, pos up
f_nrml= 5888.6 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Now to find aspect-ratio multiplier for LEFT WING 1:
   el # 0, clQ= 1297.9, el arm= 0.50, clQ_total= 1297.9, clQ_x_arm= 648.9
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 1:
   el # 0, clQ= 1306.7, el arm= 0.50, clQ_total= 1306.7, clQ_x_arm= 653.3
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 2:
   el # 0, clQ= 445.4, el arm= 0.50, clQ_total= 445.4, clQ_x_arm= 222.7
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 2:
   el # 0, clQ= 434.1, el arm= 0.50, clQ_total= 434.1, clQ_x_arm= 217.1
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 3:
   el # 0, clQ= 25.0, el arm= 0.50, clQ_total= 25.0, clQ_x_arm= 12.5
   el # 1, clQ= 25.3, el arm= 1.50, clQ_total= 50.2, clQ_x_arm= 50.4
      loc= 0.5015, AR_mult= 0.9985

Now to find aspect-ratio multiplier for RIGT WING 3:
   el # 0, clQ= 16.7, el arm= 0.50, clQ_total= 16.7, clQ_x_arm= 8.3
   el # 1, clQ= 17.0, el arm= 1.50, clQ_total= 33.7, clQ_x_arm= 33.8
      loc= 0.5022, AR_mult= 0.9978

Now to find aspect-ratio multiplier for LEFT H STAB:
   el # 0, clQ= 745.3, el arm= 0.50, clQ_total= 745.3, clQ_x_arm= 372.6
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT H STAB:
   el # 0, clQ= 746.2, el arm= 0.50, clQ_total= 746.2, clQ_x_arm= 373.1
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for VERT STAB 1:
   el # 0, clQ= 13.6, el arm= 0.50, clQ_total= 13.7, clQ_x_arm= 6.8
      loc= 0.5000, AR_mult= 1.0000

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
FUSELAGE:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
lat arm of centroid from acf ref= 0.00 m pos right
vrt arm of centroid from acf ref= -0.06 m pos up
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with alpha, with arm running from 0.03 at 0 alpha to 0.03 at 90 alpha, currently -0.2 alpha
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with beta , with arm running from 0.03 at 0 beta to 0.03 at 90 beta , currently -0.2 beta

body front area = 0.4293 square meters
body side area for side force = 2.4606 square meters
body top area for lift force = 2.0559 square meters

infinite flow speed is vx of -0.1 vy of -0.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= -0.1 vy= -0.1 vz= 29.6 m/s in the aircraft axis coordinate system

mach multiplication = 1.0038, part_cd= 0.0080, cd_cylinder= 1.0038
air attacking aft from ahead= 29.6 m/s.
air attacking up from below = -0.1 m/s.
air attacking to the right = -0.1 m/s.
alph= -0.2
beta= -0.2
angl= 0.3
cl vert=-0.0036, ref area of 2.0559, v= 29.6, rho= 1.1876, SUBSONIC body force= -3.9 N
cl side=-0.0035, ref area of 2.4606, v= 29.6, rho= 1.1876, SUBSONIC body force= -4.5 N
cd_frnt= 0.0081, ref area of 0.4294, v= 29.6, rho= 1.1876, SUBSONIC body force= 1.8 N

THIS BODY AT MACH= 0.0874
body drag force= 1.8 N (is CD of 0.0081 based on frontal area)
body side force= -4.5 N (is CL of -0.0035 based on side area)
body lift force= -3.9 N (is CL of -0.0036 based on top area)

LIFT at the centroid for alpha:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= -3.9 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LIFT at the centroid for alpha
f_axil= 175.5 N, pos aft, L= 0.8 N-m, pos right
f_side= -10.9 N, pos right, M= 175.1 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

SIDE at the centroid for beta:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= -4.5 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
SIDE at the centroid for beta
f_axil= 175.5 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 175.1 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.2 N-m, pos right
----------------------------------------------------------------------------------------------------

DRAG at the aero centroid:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 1.8 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
DRAG at the aero centroid
f_axil= 177.3 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 175.0 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.2 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #2, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0334 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 4.4 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 0.00 -0.18 3.80 m

landing gear:

x= 0.00 m pos right.
y= -0.18 m pos up.
z= 3.80 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 4.4 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= 181.7 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.3 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #3, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.2 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= -8.87 0.44 -0.16 m

landing gear:

x= -8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= 181.9 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.4 N-m, pos up
f_nrml= 5884.7 N, pos up, N= -1.9 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #4, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.2 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 8.87 0.44 -0.16 m

landing gear:

x= 8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0000 1.0000 0.0038
drag vector xyz=-0.0037 -0.0038 1.0000
side vector xyz= 1.0000 -0.0000 0.0037

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After water skimming forces:
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

I am adding mass for the jett load! Adding 200.0 kg, at long= -0.09 lat= 0.00 vert= 0.00, and changing the moments to:
L= 0.0 N-m, pos right
M= -173.6 N-m, pos up
N= 0.5 N-m, pos right

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After shifted mass forces:
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

I am adding mass for the fuel! Adding 0.0 kg, at long= -2.23 lat= 0.00 vert= -0.06, and changing the moments to:
L= -0.0 N-m, pos right
M= -173.7 N-m, pos up
N= 0.5 N-m, pos right

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After fuel mass forces:
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After engine sep mass forces:
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After weapon mass forces:
f_axil= 182.1 N, pos aft, L= 1.0 N-m, pos right
f_side= -15.4 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5884.7 N, pos up, N= 0.3 N-m, pos right
----------------------------------------------------------------------------------------------------

  ••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••GRAND TOTALS AT END OF FORCE AND MOMENT BUILD-UP•••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••

•••FINAL PROPULSIVE (ENGINE) FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL GEAR FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)••••••••••••••••••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••••••••••
f_side = -15.4 N, pos right
f_vertical= 5884.7 N, pos up
f_axial = 182.1 N, pos aft

L = 1.0 N-m, pos right
M = 174.5 N-m, pos up
N = 0.3 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG FLIGTH PATH AXIS (pos aft/right/up)••••••••••••••••••••••••••••••
f_side = -14.7 N, pos right
f_lift = 5885.3 N, pos up
f_drag = 159.6 N, pos aft

•••FINAL FORCES BEFORE ASSYMETRIC LOADING EFFECTS, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••
f_side = -15.4 N, pos right
f_vertical= 5884.7 N, pos up
f_axial = 182.1 N, pos aft

L = 1.0 N-m, pos right
M = 0.8 N-m, pos up
N = 0.7 N-m, pos right

•••MASSES TO GET FROM FORCES TO ACCELERATIONS•••••••••••••••••••••••••••••••••••••••••••••••••••••••
mass = 599.2 kg (ice accretion will change mass and MI if present!
roll MI = 2616.6 kg-m-m... M/mi=accel in RADIANS per sec
pitch MI = 335.3 kg-m-m... M/mi=accel in RADIANS per sec
yaw MI = 233.3 kg-m-m... M/mi=accel in RADIANS per sec

•••FINAL TOTAL LINEAR ACCELS, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••••••
a_x= 0.2 m/ss
a_y= 0.0 m/ss
a_z= 0.2 m/ss

•••FINAL TOTAL ANGULAR ACCELS, ABOUT AIRCRAFT AXIS (pos right/up/right)•••••••••••••••••••••••••••••
Pdot (roll) = 0.0 deg/ss
Qdot (pitch)= 0.0 deg/ss
Rdot (yaw) = 0.0 deg/ss

•••FINAL TOTAL LINEAR VELOCITIES, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••
v_x= 27.9 m/s
v_y= -1.0 m/s
v_z= -10.0 m/s